Possible
Intercept point
speed v
1. Solve for t where t>0
||r + v * t|| = s * t
2. calculate aim point target_pos + v * t
3. desired heading is
Aim point – interceptor pos
speed
s
Relative position
 r

---
Potential Issues
- Simulation Fidelity vs. Real Aerodynamics (wake turbulance, nonlinear aerodynamics)
- Sensor Assumptions vs. Operational Reality
- Target Behavior Modeling
- Actuator and Control Constraints Ignored or Idealized
- Transition Between Radar and Vision Guidance
- Environmental Effects Not Modeled (wind shear, gusts…)