Possible
Intercept point
speed v
1. Solve for t where t>0
||r + v * t|| = s * t
2. calculate aim point target_pos + v * t
3. desired heading is
Aim point – interceptor pos
speed
s
Relative position
 r

---
Potential Issues
- Bigger evasive maneuvers
- Greater speed difference
- Evasive maneuvers just before impact